| the information contained in this drawing shall not be reproduced in any form without permission in writing from solartron metrology ltd. ( 2003 |
| --- |
| solartron metrology ltd., steyning way, bognor regis, sussex, england, po22 9st |
| tolerances unless otherwise stated |  |
| hole diameters size to plus. |  |
| dimensions in mm |  |
|  | Name | Signature | Date |
| Original Author | Refer to original EDCR |  | 11/08/2003 |
| Last Modified by | Phil Townsend |  | 23/02/2016 |
| Approved by | Graham Davis |  | 24/02/2016 |
| FOR EFFECTIVITY DATE REFER TO EDCR |
| 25 | 22233 | Option DA12 (-2 to +2 V) added |
| 24 | 19217 | Updated for Orbit3 |
| 23 | 18909 | Cable lengths added – 3m up to 5m |
| 22 | 18807 | Pin out for Voltage connection option 05 added |
| 21 | 18689 | Pin out for PT100 connection option 03 added. |
| 20 | 18670 | Pin Out 06 added (compatible to Seewald pressure sensor (type PR33X/3bar/81306.10) |
| 19 | 18449 | Current connection option added to 03 |
| 18 | 18302 | 05 Wiring added for PT100 |
| 17 | 17663 | Rationalisation of wiring |
| 16 | 17663 | 4-20 mA (non loop) added. Titles amended |
| 15 | 17292 | Connections option 05 clarified |
| 14 | 17257 | Addition of extra cable lengths (1.5 ; 2.0 ; 2.5) |
| 13 | 16917 | Addition of 3 m cable length |
| 12 | 16975 | Addition of option 11 to configurator |
| 11 | 16755 | Clarification of pin colours. Pin option for 01 added. |
| 10 | 16773 | Addition of Pinout for 3-pin plug 4-20 mA |
| 9 | 16756 | Addition of Euraltech (Mecalix) connections + 5-way DIN Socket |
| Issue | EDCR | Change Comments - for detailed information refer to EDCR. |
| Document summary: |
| Analogue Input Module Ordering Guide |
| Document Types: WI, OP, FORM, PS, TS, ES |
| Title | Number |
| Analogue Input Module Ordering Guide | 502517 |

ALL COPIES OF THIS DOCUMENT MUST BE CONFIRMED AS LATEST ISSUE

| Form No: | 502517 | Analogue Input Module Ordering Guide |
| --- | --- | --- |

|  | D | A |  |  |  |  |  |  |  |  |  |  |  |  | -3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Input – xx |  |  |  |  |
| 0 | 0 |  | 4 to 20 mA | 1 | 0 |  | PT100 –50 to +850 (C |  |  |
| 0 | 1 |  | 0 to +5 V | 1 | 1 |  | PT100 –20 to +70 (C |  |  |
| 0 | 2 |  | 0 to +10 V | 1 | 2 |  | -2 to +2 V |  |  |
| 0 | 3 |  | -5 to +5 V |  |  |  |  |  |  |
| 0 | 4 |  | -10 to +10 V |  |  |  |  |  |  |
| 0 | 5 |  | ±20 mA |  |  |  |  |  |  |
| 0 | 6 |  | 4 to 20 mA Current Loop |  |  |  |  |  |  |
| 0 | 7 |  | 0 to +24 V |  |  |  |  |  |  |
| 0 | 8 |  | -1 to +1 V |  |  |  |  |  |  |
| 0 | 9 |  | PT100 –50 to +250 (C |  |  |  |  |  |  |
| Cable Length – a.bc (m) |  |  |  |
| 0 | 1 | 5 |  | 0.15m | 1 | 5 | 0 |  | 1.50m | 3 | 5 | 0 |  | 3.50m * |  |
| 0 | 3 | 0 |  | 0.30m | 2 | 0 | 0 |  | 2.00m | 4 | 0 | 0 |  | 4.00m * |  |
| 0 | 5 | 0 |  | 0.50m | 2 | 5 | 0 |  | 2.50m | 4 | 5 | 0 |  | 4.50m * |  |
| 1 | 0 | 0 |  | 1.00m | 3 | 0 | 0 |  | 3.00m | 5 | 0 | 0 |  | 5.00m * |  |
| NB: Longer cable lengths may affect performance. If in doubt, check with Sales Office or Distributor. | * These lengths are not suitable for types DA08, DA09, DA10 and DA11. |  |
| Cable Type – x |  |  |
| 1 |  | PUR – Black (was Green on Oribt2) |
| 2 |  | Braided |
| 3 |  | Pur – Black |
| Connections - yy |  |
| 0 | 0 |  | Flying Leads |

| 0 | 1 |  | 3 Way 180( DIN Plug | Current/Current Loop | +/- Voltage Pin Out |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Pin 1 | Black (Common) | Pin 1 | White (Positive Input) |
|  |  |  |  | Pin 2 | Yellow (Loop supply) | Pin 2 | Black (Common) |
|  |  |  |  | Pin 3 | Green (Input) | Pin 3 | Blue (Negative Input) |
|  |  |  |  | Case | Screen | Case | Screen |

| 0 | 2 |  | 3 Way 180( |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | DIN Socket |  |  |  |  |

| 0 | 3 |  | 5 Way 240( DIN Plug | Current/Current Loop | +/- Voltage Pin Out |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Pin 1 | Yellow (Loop supply) | Pin 3 | Blue (Negative Input) |
|  |  |  |  | Pin 2 | Green (Input) | Pin 4 | Black (0V) |
|  |  |  |  | Pin 3 | Black (Common) | Pin 5 | White (Positive Input) |
|  |  |  |  | Case | Screen | Case | Screen |
|  |  |  |  | PT100 |  |  |
|  |  |  |  | Pin 1 | Red ((2.5V reference) |  |  |
|  |  |  |  | Pin 2 | Blue (-ve voltage input) |  |  |
|  |  |  |  | Pin 3 | Black (0V common) |  |  |
|  |  |  |  | Pin 5 | White (+ve voltage input) |  |  |
|  |  |  |  | Case | Screen |  |  |

| 0 | 4 |  | Euraltech (Mecalix) label 5 Pin | Current/Current Loop (Euraltech) | 0-Voltage Pin Out (Euraltech) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Pin 1 | Yellow (Loop supply) | Pin 4 | Blue (Negative Input) |
|  |  |  |  | Pin 2 | Green (Input) | Pin 4 | Black (0V) |
|  |  |  |  | Pin 3 | Black (Common) | Pin 5 | White (Positive Input) |
|  |  |  |  | Case | Screen | Case | Screen |

| 0 | 5 |  | 5 Way 240( DIN Socket | Current/Current Loop | +/- Voltage Pin Out |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Pin 1 | Yellow (Loop supply) | Pin 3 | Blue (Negative Input) |
|  |  |  |  | Pin 2 | Green (Input) | Pin 4 | Black (0V) |
|  |  |  |  | Pin 3 | Black (Common) | Pin 5 | White (Positive Input) |
|  |  |  |  | Case | Screen | Case | Screen |
|  |  |  |  | PT100 |  |  |
|  |  |  |  | Pin 1 | Red ((2.5V reference) |  |  |
|  |  |  |  | Pin 2 | Blue (-ve voltage input) |  |  |
|  |  |  |  | Pin 3 | Black (0V common) |  |  |
|  |  |  |  | Pin 5 | White (+ve voltage input) |  |  |
|  |  |  |  | Case | Screen |  |  |

ALL COPIES OF THIS DOCUMENT MUST BE CONFIRMED AS LATEST ISSUE

| Form No: | 502517 | Analogue Input Module Ordering Guide |
| --- | --- | --- |

| 0 | 6 |  | 5 Way 240° DIN Socket | Current/Current Loop |  |
| --- | --- | --- | --- | --- | --- |
| Compatible to Seewald pressure sensor (type PR33X/3bar/81306.10) |  | Pin 1 | GND Black (Common) |  |  |
|  |  | Pin 2 | Output 4-20mA Green (input) |  |  |
|  |  | Pin 3 | Vcc Yellow (loop supply) |  |  |
|  |  | Case | Screen |  |  |

| Analogue Input Module Description |
| --- |
|  |  |  |  | RANGE INFO |  |  | Termination | Use these characters as required for special information |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 |
| A | I | M |  | 0 | - | 5 | V |  |  |  |  | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | 0 | - | 1 | 0 | V |  |  |  | P | L |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | 0 | - | 2 | 4 | V |  |  |  | S | K | T |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | + | / | - | 1 | V |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | + | / | - | 5 | V |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | + | / | - | 1 | 0 | V |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | 4 | - | 2 | 0 | m | A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | + | / | - | 2 | 0 | m | A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| A | I | M |  | P | T | 1 | 0 | 0 |  | - | 5 | 0 |  | T | O |  | + | 2 | 5 | 0 | D | E | G | C |  | W |  |
| A | I | M |  | P | T | 1 | 0 | 0 |  | - | 5 | 0 |  | T | O |  | + | 8 | 5 | 0 | D | E | G | C |  | W |  |

# Text boxes

(Denotes Orbit3)